Instructions for preparing, removing and shipping Fiessler AKAS lasers for repair

When you want to send the Fiessler AKAS system here is what to do.

Have your people mark the position of the steel backing plate that is used to attach the aluminum arm to the mounting structure. By doing this you will be able to re-install the arms and make the alignment much easier.

Remove the black plastic cover on the top of each arm by removing and then saving the 4 Phillips screws in each corner. Unplug each connector. Each is color coded and differently configured so they can’t be plugged back in wrong. Secure the wiring harness in such a way that they won’t be damaged or contaminated.

Slightly loosen the table screws that help hold the arms in position on the left and right. Do not touch the other screws.

Grab the extrusion from the bottom & while using a 4mm Allen wrench loosen the 4 corner screws in the steel backing plate. It only takes one complete turn to loosen them.

Carefully slide the extrusion downward out of the holder.

Follow the same procedure for the other device. We don’t need mounting hardware!

Wrap and package the devices to avoid shipping damage. Include paperwork identifying a contact by phone and email, include a brief description of the failure and your carrier’s account number for cheaper rates on return shipping.

Ship with your preferred carrier (add andrew@pressbrakesafety.com to the ship notifications)

Andrew Litton

5693 Federalist Ct.

Indianapolis, IN 46254